## Hardness

Hardness in water is defined as the presence of multivalent cations. Hardness in water can cause water to form scales and a resistance to soap. It can also be defined as water that doesn’t produce lather with soap solutions, but produces white precipitate (scum). Example :

2C17H35COONa + Ca2+ → (C17H35COO)2Ca + 2Na+

## [edit] Types of hard water

In the 1960s, scientist Chris Gilby discovered that hard water can be categorized by the ions found in the water.[citation needed] A distinction is also made between 'temporary' and 'permanent' hard water.

### [edit] Temporary hardness

Temporary hardness is caused by a combination of calcium ions and bicarbonate ions in the water. It can be removed by boiling the water or by the addition of lime (calcium hydroxide). Boiling promotes the formation of carbonate from the bicarbonate and precipitates calcium carbonate out of solution, leaving water that is softer upon cooling.

The following is the equilibrium reaction when calcium carbonate (CaCO3) is dissolved in water:

CaCO3(s) + H2CO3(aq) ⇋ Ca2+(aq) + 2HCO3-(aq)

Upon heating, less CO2 is able to dissolve into the water (see Solubility). Since there is not enough CO2 around, the reaction cannot proceed from left to right, and therefore the CaCO3 will not dissolve as rapidly. Instead, the reaction is forced to the left (i.e. products to reactants) to re-establish equilibrium, and solid CaCO3 is formed. Boiling the water will remove hardness as long as the solid CaCO3 that precipitates out is removed. After cooling, if enough time passes the water will pick up CO2 from the air and the reaction will again proceed from left to right, allowing the CaCO3 to "re-dissolve" into the water.

For more information on the solubility of calcium carbonate in water and how it is affected by atmospheric carbon dioxide, see calcium carbonate.

### [edit] Permanent hardness

Permanent hardness is hardness (mineral content) that cannot be removed by boiling. It is usually caused by the presence of calcium and magnesium sulfates and/or chlorides in the water, which become more soluble as the temperature rises. Despite the name, permanent hardness can be removed using a water softener or ion exchange column, where the calcium and magnesium ions are exchanged with the sodium ions in the column.

Hard water causes scaling, which is the left over mineral deposits that are formed after the hard water had evaporated. This is also known as limescale. The scale can clog pipes, ruin water heaters, coat the insides of tea and coffee pots, and decrease the life of toilet flushing units.

Similarly, insoluble salt residues that remain in hair after shampooing with hard water tend to leave hair rougher and harder to untangle. [1]

In industrial settings, water hardness must be constantly monitored to avoid costly breakdowns in boilers, cooling towers, and other equipment that comes in contact with water. Hardness is controlled by the addition of chemicals and by large-scale softening with zeolite and ion exchange resins.

## [edit] Measurement

It is possible to measure the level of hard water by obtaining a free water testing kit. These are supplied by most water softening companies. There are several different scales used to describe the hardness of water in different contexts.

- Parts per million (ppm)
Usually defined as one milligram of calcium carbonate (CaCO3) per litre of water (the definition used below)[2].

- grains/gallon (gpg)
Defined as 1 grain (64.8 mg) of calcium carbonate per U.S. gallon (3.79 litres), or 17.118 ppm

- mmol/L (millimoles per litre)
One millimole of calcium (either Ca2+ or CaCO3) per litre of water corresponds to a hardness of 100.09 ppm or 5.608 dGH, since the molar mass of calcium carbonate is 100.09 g/mol.

- Degrees of General Hardness (dGH)
One degree of General Hardness is defined as 10 milligrams of calcium oxide per litre of water, which is the same as one German degree (17.848 ppm).

- Various obsolete "degrees":

  - Clark degrees (°Clark)/English degrees (°E)
One degree Clark is defined as one grain (64.8 mg) of calcium carbonate per Imperial gallon (4.55 litres) of water, equivalent to 14.254 ppm.

  - German degrees (Deutsche Härte, °dH)
One degree German is defined as 10 milligrams of calcium oxide per litre of water. This is equivalent to 17.848 milligrams of calcium carbonate per litre of water, or 17.848 ppm.

  - French degrees (°f) (letter to be written in lowercase to avoid confusion with degree Fahrenheit — not always adhered to)
One degree French is defined as 10 milligrams of calcium carbonate per litre of water, equivalent to 10 ppm.

  - American degrees
One degree American is defined as one milligram of calcium carbonate per litre of water, equivalent to 1 ppm.

Although most of the above measures define hardness in terms of concentrations of calcium in water, any combination of calcium and magnesium cations having the same total molarity as a pure calcium solution will yield the same degree of hardness. Consequently, hardness concentrations for naturally occurring waters (which will contain both Ca2+ and Mg2+ ions), are usually expressed as an equivalent concentration of pure calcium in solution. For example, water that contains 1.5 mmol/L of elemental calcium (Ca2+) and 1.0 mmol/L of magnesium (Mg2+) is equivalent in hardness to a 2.5 mmol/L solution of calcium alone (250.2 ppm).

Because it is the precise mixture of minerals dissolved in the water, together with the water's pH and temperature, that determines the behaviour of the hardness, a single-number scale does not adequately describe hardness. Descriptions of hardness correspond roughly with ranges of mineral concentrations:

- Very soft: 0-70 ppm, 0-4 dGH

- Soft: 70-140 ppm, 4-8 dGH

- Slightly hard: 140-210 ppm, 8-12 dGH

- Moderately hard: 210-320 ppm, 12-18 dGH

- Hard: 320-530 ppm, 18-30 dGH

- Very hard >530 ppm, >30 dGH

## Softening

Main article: water softening

It is often desirable to soften hard water, as it does not readily form lather with soap. Soap is wasted when trying to form lather, and in the process, scum forms. Hard water may be treated to reduce the effects of scaling and to make it more suitable for laundry and bathing.

### [edit] Process

A water softener, like a fabric softener, works on the principle of cation or ion exchange in which ions of the hardness minerals are exchanged for sodium or potassium ions, effectively reducing the concentration of hardness minerals to tolerable levels and thus making the water softer and giving it a smoother feeling.[13]

The most economical way to soften household water is with an ion exchange water softener. This unit uses sodium chloride (table salt) to recharge beads made of the ion exchange resins that exchange hardness mineral ions for sodium ions. Artificial or natural zeolites can also be used. As the hard water passes through and around the beads, the hardness mineral ions are preferentially absorbed, displacing the sodium ions. This process is called ion exchange. When the bead or sodium zeolite has a low concentration of sodium ions left, it is exhausted, and can no longer soften water. The resin is recharged by flushing (often back-flushing) with saltwater. The high excess concentration of sodium ions alter the equilibrium between the ions in solution and the ions held on the surface of the resin, resulting in replacement of the hardness mineral ions on the resin or zeolite with sodium ions. The resulting saltwater and mineral ion solution is then rinsed away, and the resin is ready to start the process all over again. This cycle can be repeated many times.

The discharge of brine water during this regeneration process has been banned in some jurisdictions (notably California, USA) due to concerns about the environmental impact of the discharged sodium.

Potassium chloride (softener salt substitute) may also be used to regenerate the resin beads. It exchanges the hardness ions for potassium. It also will exchange naturally occurring sodium for potassium resulting in sodium-free soft water.

Some softening processes in industry use the same method, but on a much larger scale. These methods create an enormous amount of salty water that is costly to treat and dispose of.

Temporary hardness, caused by hydrogen carbonate (or bicarbonate) ions, can be removed by boiling. For example, calcium bicarbonate, often present in temporary hard water, may be boiled in a kettle to remove the hardness. In the process, a scale forms on the inside of the kettle in a process known as "furring". This scale is composed of calcium carbonate.

Ca(HCO3)2 → CaCO3 + CO2 + H2O

Hardness can also be reduced with a lime-soda ash treatment. This process, developed by Thomas Clark in 1841, involves the addition of slaked lime (calcium hydroxide — Ca(OH)2) to a hard water supply to convert the hydrogen carbonate hardness to carbonate, which precipitates and can be removed by filtration:

Ca(HCO3)2 + Ca(OH)2 → 2CaCO3 + 2H2O

The addition of sodium carbonate also permanently softens hard water containing calcium sulfate, as the calcium ions form calcium carbonate which precipitates out and sodium sulfate is formed which is soluble. The calcium carbonate that is formed sinks to the bottom. Sodium sulfate has no effect on the hardness of water.

Na2CO3 + CaSO4 → Na2SO4 + CaCO3

### Effects on skin

Some confusion may arise after a first experience with soft water. Hard water does not lather well with soap and leaves a "less than clean" feeling. Soft water lathers better than hard water but leaves a "slippery feeling" on the skin after use with soap. A certain water softener manufacturer contends that the "slippery feeling" after showering in soft water is due to "cleaner skin" and the absence of "friction-causing" soap scum.

However, the chemical explanation is that softened water, due to its sodium content, has a much reduced ability to combine with the soap film on your body and therefore, it is much more difficult to rinse off.[14] Solutions are to use less soap or a synthetic liquid body wash.

# Hydrogen sulfide

Hydrogen sulfide (or hydrogen sulphide) is the chemical compound with the formula H2S. This colorless, toxic and flammable gas is partially responsible for the foul odor of rotten eggs and flatulence.

It often results from the bacterial break down of sulfates in organic matter in the absence of oxygen, such as in swamps and sewers (anaerobic digestion). It also occurs in volcanic gases, natural gas and some well waters. The odor of H2S is commonly misattributed to elemental sulfur, which is in fact odorless. Hydrogen sulfide has numerous names, some of which are archaic (see table).

## Production

Hydrogen sulfide is obtained by its separation from sour gas, that is natural gas with high content of H2S. It can be produced by reacting hydrogen gas with molten elemental sulfur at about 450 °C. Hydrocarbons can replace hydrogen in this process.[1]

Sulfate-reducing bacteria produce hydrogen sulfide under ambient conditions by the reduction of sulfate or from elemental sulfur.

The standard lab preparation is to gently heat iron sulfide (FeS) with a strong acid in a Kipp generator.

A less well known and more convenient alternative is to react aluminum sulfide with water:

H2O + Al2S3 → H2S + Al2O3.

## Occurrence

Deposit of sulfur on a rock, caused by volcanic gases

Small amounts of hydrogen sulfide occur in crude petroleum but natural gas can contain up to 90%. Volcanoes and hot springs emit some H2S, where it probably arises via the hydrolysis of sulfide minerals, i.e. MS + H2O → MO + H2S. Normal concentration in clean air is about 0.0001-0.0002 ppm.[citation needed]

About 10% of total global emissions of H2S are due to human activity. By far the largest industrial route to H2S occurs in petroleum refineries: the hydrodesulfurization process liberates sulfur from petroleum by the action of hydrogen. The resulting H2S is converted to elemental sulfur by partial combustion via the Claus process, which is a major source of elemental sulfur. Other anthropogenic sources of hydrogen sulfide include coke ovens, paper mills (using the sulfate method), and tanneries. H2S arises from virtually anywhere where elemental sulfur comes into contact with organic material, especially at high temperatures.

Hydrogen sulfide can be present naturally in well water. In such cases, ozone is often used for its removal. An alternative method uses a filter with manganese dioxide. Both methods oxidize sulfides to less toxic sulfates.

A buildup of hydrogen sulfide in the atmosphere could have caused the Permian-Triassic extinction event 252 million years ago.[2]

### In analytical chemistry

Hydrogen sulfide used to have importance in analytical chemistry for well over a century, in the qualitative inorganic analysis of metal ions. For such small-scale laboratory use, H2S was made as needed in a Kipp generator by reaction of sulfuric acid (H2SO4) with ferrous sulfide FeS. Kipp generators were superseded by the use of thioacetamide, an organic solid that converts in water to H2S. In these analyses, heavy metal (and nonmetal) ions (e.g. Pb(II), Cu(II), Hg(II), As(III)) are precipitated from solution upon exposure to H2S. The components of the resulting precipitate redissolve with some selectivity.